## Slide 1: ACA Final Project

## Slide 2: Improving memory subsystem performance of RISC-V Sodor processor
Cache
50 cycles per read/write

## Slide 3: Overview
Baseline: No cache
Each team could decide what features to add to improve memory system performance
  E.g., non-blocking cache, victim cache, multi-level cache, prefetch etc.
Projects will be judged based on
  what features you add to enhance the baseline, and
  Miss rate & overall performance
3-person team

## Slide 5: Compile & Run Emulator (1/2)
Please clone the repo again!!
Clone repo
  git clone https://github.com/chenchc/riscv-sodor.git
  cd riscv-sodor
  git submodule update --init --recursive
Compiling front-end server (will install RISC-V front-end server library under ${RISCV_FESV})
  cd riscv-fesvr
  ./configure --prefix=/usr/local
  make install

## Slide 6: Compile & Run Emulator (2/2)
Build the sodor emulators
  $cd ..
  $ ./configure --with-riscv=/usr/local
  $ make
All processors are installed under the directory “riscv-sodor/emulator”
Run all processors
  make run-emulator
Run a specific processor
  cd emulator/${PROCESSOR_NAME}
  make run

## Slide 7: Profiling Results
When you type “make run” in riscv-sodor/emulator/rv32_5stage, you should see:
FREEZE: Pipeline stall due to cache miss
Extended metrics you can use to evaluate your cache

## Slide 8: Baseline
See riscv-sodor/src/rv32_5stage/dcache.scala
Baseline: Just pass through…
Modify this line to integrate your own cache

## Slide 9: Reference
Chisel tutorial
  Provided on ceiba
Must-see codes in sodor:
  riscv-sodor/src/common/memory.scala

## Slide 10: Update (6/11)

## Slide 11: Changelog
Tons of bugs fixed (see commit logs)
Burst Read/Write with 64 byte data width
Please run git pull to update the repo (or simply clone it again…)

## Slide 12: Burst Read
In src/common/memory.scala
  The memory reply interface MemResp now contains burst_data which is a 16-element vector with words (4 byte) filled
  burst_data will be well aligned to 64 bytes and contain the desired data.
    Request address doesn’t need to be aligned.
    The desired data may be somewhere in the burst_data vector, depending on the address.
  Fully compatible with previous mechanism (Single data read)

## Slide 13: Example to leverage burst read
In src/rv32_5stage/dcache.scala
  Read burst data
  Calculate the position of the requested data
  Extract the word out
  Use LoadDataGen helper function to perform byte, half load or padding
  (LoadDataGen and other useful functions are provided in src/common/memory.scala)

## Slide 14: Burst Write
In src/common/memory.scala
  Add a new memory operation - M_XWRBURST
  Add a new datapath burst_data in memory request interface
  Usage: Assign appropriate arguments on MemReq with typ=M_XWRBURST and burst_data.

## Slide 15: Any question? Or bugs?
You can raise an issue on Github: https://github.com/chenchc/riscv-sodor
Or send mails to: bryan830401@gmail.com